## Slide 1: IE1020 Network Fundamentals
Group Number: MLB_WD_CSNE_01.01_05

## Slide 2
          Introduction
          Logical Topology
          Physical Topology
          Devices
          Media Types
          LAN / WAN Technologies
          Protocols
          IP Addressing Schema
Content

## Slide 3
INTRODUCTION
XYZ University is a large university with 7 branches located throughout the country. The university has over 50,000 students, faculty, and staff members who rely heavily on the university's network for research, communication, and learning. The university's IT department is responsible for designing and maintaining the network infrastructure for all the campuses.

## Slide 4
LOGICAL TOPOLOGY
RANAWAKA R A S M IT22320728

## Slide 5
LOGICAL TOPOLOGY
Logical topology refers to the way in which devices & systems are logically interconnected in a computer network. It describes the path that data follows as it travels between devices & the logical arrangement of those devices. Logical topology focuses on the flow of information & how devices communicate with each other.

## Slide 6
LOGICAL TOPOLOGY

## Slide 7
LOGICAL TOPOLOGY
    CORE LAYER
    ACCESS LAYER
    DISTRIBUTION LAYER

## Slide 8
LOGICAL TOPOLOGY
Access layer has end devices and switches. The IT department is in the main building. The distribution layer in every building has multiple switches to make the data redundant & act as a backup in case one fails. In addition, it contains a firewall which obstructs unauthorized access. The building resides in the main building, where it collaborates with the other branches because every branch has a core router which is interconnected to the main router.

## Slide 9
Physical TOPOLOGY
DEWARATHNE P S IT22004536

## Slide 10
PHYSICAL TOPOLOGY

## Slide 11
PHYSICAL TOPOLOGY

## Slide 12
PHYSICAL TOPOLOGY

## Slide 13
PHYSICAL TOPOLOGY

## Slide 14
Devices
HASARA M K IT22308566

## Slide 15
DEVICES
1 ) Access Network
Cisco catalyst 2960-x series switches
Basically, designed for small and medium-sized businesses and campus networks.
Offer a range of features and capabilities to enhance network performance, security and manageability.
Provides multiple gigabit ethernet ports for high-speed connectivity.
Include features like DHCP snooping, IP source guard etc.

## Slide 16
DEVICES
2) Distribution Network
Cisco Catalyst 3850 Series switches
Advanced and fixed-configuration switches.
Designed for enterprise networks.
Offers a wide range of features and capabilities for enhanced network performance, security and management.
Offering high-speed connectivity with options for gigabit ethernet, multigigabit ethernet and 10-gigabit ethernet ports.
Support IP phones, wireless access points and surveillance cameras.

## Slide 17
2) Distribution Network
Cisco ASA firewall
It provides firewall, intrusion prevention, and virtual private network (VPN) capabilities to protect networks and applications from unauthorized access and security threats.
Acts as a network firewall.
Remains a widely deployed and supported firewall solution.
DEVICES

## Slide 18
3) Core Network
Cisco Catalyst 9500 Series switches
Designed for High performance, feature-rich and expandable for enterprise networks.
Commonly used in large-scale deployments.
DEVICES

## Slide 19
3) Core Network
Cisco ASR 9000 Series routers
Family of routers designed for high-performance, carrier-grade networking and service provider environments
Offer large scalability options to serve growing network requirements.
Feature a modular design, allowing for flexibility and expansion
Offer scalability, reliability, and advanced features.
DEVICES

## Slide 20
4) Wireless Network
Cisco Aironet 3800 Series access points
Family of high-performance wireless access points designed for enterprise deployments
Provide fast, reliable Wi-Fi connectivity with advanced features to support demanding wireless networks.
These access points support multigigabit Ethernet interfaces, such as 2.5 Gigabit Ethernet and 5 Gigabit Ethernet.
DEVICES

## Slide 21
Media Types
GONAGALA G A S T IT22314956

## Slide 22
MEDIA TYPES
1) CAT 6/ CAT 6A cables
Provide excellent performance, supporting Gigabit Ethernet speeds and beyond.
Reliable and high-quality data transmission.
Widely available and cost-effective.
RJ-45 connectors, guarantee a secure and standardized connection.

## Slide 23
MEDIA TYPES
2) WiFi 6 (802.11ax) standard
Offer high-speed wireless connections, improved capacity, and enhanced security features.
Faster and more dependable wireless connections
Better performance in crowded environments with multiple devices.

## Slide 24
LAN / WAN TECHNOLOGIES
GONAGALA G A S T IT22314956

## Slide 25
LAN / WAN TECHNOLOGIES
LAN Technologies
Giga - Ethernet
IEEE802.3ab standardize Giga-Ethernet over UTP using CAT-6 cables.
Gigabit Ethernet enables high speeds up to 1000 Mbps throughout each campus building, allowing for rapid data transmission, communication, and resource sharing among devices.
Offers the scalability and performance required to support many users and devices at the University.

## Slide 26
LAN / WAN TECHNOLOGIES
WAN Technologies
Point-to-point (P2P) leased lines
P2P leased lines create dedicated connections between branches, providing secure and high-bandwidth communications.
Ensure constant and reliable communication between campuses, allowing for effective resource sharing, data transfer, and branch collaboration.

## Slide 27
Protocols
PERERA P A I P IT22884824

## Slide 28
PROTOCOLS
LAYER | PROTOCOLS
(7) Application Layer | HTTP, SMTP, DNS, FTP
(6) Presentation Layer | SSL, TLS
(5) Session Layer | NetBIOS, SSH, SIP, RTP
(4) Transport Layer | TCP, UDP
(3) Network Layer | IPv4, IPv6, ICMP, OSPF, EIGRP
(2) Data Link Layer | Ethernet (IEEE 802.3), IEEE 802.1X, Wi-Fi (IEEE 802.11)
(1) Physical Layer | Ethernet (IEEE 802.3), Wi-Fi (IEEE 802.11)
LAYER
(7) Application Layer
(6) Presentation Layer
(5) Session Layer
(4) Transport Layer
(3) Network Layer
(2) Data Link Layer
(1) Physical Layer

## Slide 29
PROTOCOLS
LAYER
(7) Application Layer
(6) Presentation Layer
(5) Session Layer
(4) Transport Layer
(3) Network Layer
(2) Data Link Layer
(1) Physical Layer
LAYER | PROTOCOLS
(7) Application Layer | HTTP, SMTP, DNS, FTP
(6) Presentation Layer | SSL, TLS
(5) Session Layer | NetBIOS, SSH, SIP, RTP
(4) Transport Layer | TCP, UDP
(3) Network Layer | IPv4, IPv6, ICMP, OSPF, EIGRP
(2) Data Link Layer | Ethernet (IEEE 802.3), IEEE 802.1X, Wi-Fi (IEEE 802.11)
(1) Physical Layer | Ethernet (IEEE 802.3), Wi-Fi (IEEE 802.11)
Application – HTTP, SMTP, DNS, FTP. These protocols enable web browsing, email communication, domain name resolution, and file transfer services within the campus network.
Presentation - SSL/TLS for secure communication and encryption of data, preventing unauthorized access within the campus network.
Session – NetBIOS, SSH, SIP, RTP. These protocols establish and manage sessions between network devices for communication and remote access.

## Slide 30
PROTOCOLS
LAYER | PROTOCOLS
(7) Application Layer | HTTP, SMTP, DNS, FTP
(6) Presentation Layer | SSL, TLS
(5) Session Layer | NetBIOS, SSH, SIP, RTP
(4) Transport Layer | TCP, UDP
(3) Network Layer | IPv4, IPv6, ICMP, OSPF, EIGRP
(2) Data Link Layer | Ethernet (IEEE 802.3), IEEE 802.1X, Wi-Fi (IEEE 802.11)
(1) Physical Layer | Ethernet (IEEE 802.3), Wi-Fi (IEEE 802.11)
Transport - TCP (Transmission Control Protocol) for reliable, connection-oriented data transfer. UDP (User Datagram Protocol) for fast, connectionless data transfer over the campus network
  TCP – accessing shared resources / submitting assignments.
  UDP – Video Streaming / Online Learning Session
Network Layer – IP (IPv4 and IPv6) for addressing and routing packets between networks.
OSPF (Open Shortest Path First) or EIGRP (Enhanced Interior Gateway Routing Protocol) for dynamic routing within the university network

## Slide 31
PROTOCOLS
LAYER | PROTOCOLS
(7) Application Layer | HTTP, SMTP, DNS, FTP
(6) Presentation Layer | SSL, TLS
(5) Session Layer | NetBIOS, SSH, SIP, RTP
(4) Transport Layer | TCP, UDP
(3) Network Layer | IPv4, IPv6, ICMP, OSPF, EIGRP
(2) Data Link Layer | Ethernet (IEEE 802.3), IEEE 802.1X, Wi-Fi (IEEE 802.11)
(1) Physical Layer | Ethernet (IEEE 802.3), Wi-Fi (IEEE 802.11)
Data Link - Ethernet (IEEE 802.3) for framing and transmitting data over the local network. IEEE 802.1X for port-based network access and IEEE 802.11 provides wireless communication.
Physical - Ethernet (IEEE 802.3) for the physical transmission of data over the network and IEEE 802.11 for wireless communication.
Ethernet
  10 Mbps
  100 Mbps (Fast Ethernet)
  1 Gbps (Gigabit Ethernet)
  10 Gbps (10 Gigabit Ethernet)
Wireless (IEEE 802.11)
  802.11b
  802.11g
  802.11n
  802.11ac
  802.11ax

## Slide 32
IP ADDRESSING SCHEMA
PERERA P A I P IT22884824

## Slide 33
IP Addressing SCHEMA
Main Campus – 16,000
1, 2, 3 branches – 8,000
4, 5, 6, 7 branches – 4,000
It provides 65,536 Ip addresses.
Major Network - 172.16.0.0 / 16

## Slide 34
IP Addressing SCHEMA
Subnet name | Needed Size | Allocated Size | Address | Mask | Assignable Range | Broadcast
Main Campus | 16000 | 16382 | 172.16.0.0 | /18 | 172.16.0.1 - 172.16.63.254 | 172.16.63.255
Branch 1 | 8000 | 8190 | 172.16.64.0 | /19 | 172.16.64.1 - 172.16.95.254 | 172.16.95.255
Branch 2 | 8000 | 8190 | 172.16.96.0 | /19 | 172.16.96.1 - 172.16.127.254 | 172.16.127.255
Branch 3 | 8000 | 8190 | 172.16.128.0 | /19 | 172.16.128.1 - 172.16.159.254 | 172.16.159.255
Branch 4 | 4000 | 4094 | 172.16.160.0 | /20 | 172.16.160.1 - 172.16.175.254 | 172.16.175.255
Branch 5 | 4000 | 4094 | 172.16.176.0 | /20 | 172.16.176.1 - 172.16.191.254 | 172.16.191.255
Branch 6 | 4000 | 4094 | 172.16.192.0 | /20 | 172.16.192.1 - 172.16.207.254 | 172.16.207.255
Branch 7 | 4000 | 4094 | 172.16.208.0 | /20 | 172.16.208.1 - 172.16.223.254 | 172.16.223.255

## Slide 35
Group members
DEWARATHNE P S (Leader) IT22004536
RANAWAKA R A S M IT22320728
HASARA M K IT22308566
PERERA P A I P IT22884824
GONAGALA G A S T IT22314956

## Slide 36
thank you